Input file for the TRAPRB code [Jarmain&McCallum1970]
Variable descriptions found in program “FCF486.FOR” (sent by Prof. Amaury)

C... NI = 0 ALLOWS DENSITY GRAPHS TO BE PRODUCED.OTHER VALUES DO NO
C... NS GIVES ORTHOGONALITY TEST IF = 1
C... IGRAPH
C... IENERG
C... ISTATE = 2 FOR A TRANSITION = 1 FOR A SINGLE STATE
C... RMIN MINIMUM RADIUS FOR CALCULATION OF WAVEFUNCTIONS
C... RMAX MAXIMUM RADIUS FOR CALCULATION OF WAVEFUNCTIONS
C... DELR RADIAL INTERVAL FOR CALCULATION OF WAVEFUNCTIONS
C... MAXV MAXIMUM QUANTUM NUMBER FOR CALCULATION OF RESULTS
C... BE EQUILBRIUM ROTATIONAL CONSTANT
C... DE DISSOCIATION ENERGY OR ESTIMATE THEREOF
C... KDMAXV MAXIMUM QUANTUM NUMBER FOR CALCULATION OF KLEIN DUNHAM
C... POTENTIAL.MUST BE AT LEAST 2 AND NOT MORE THAN 30
C... NEIG USED FOR WORK IN THE CONTINUUM, NUMBER OF ENERGY LEVELS
C... TO CALCULATE CONTINUUM WAVEFUNCTIONS AT

C... READ IN EXPERIMENTAL EIGENVALUES AND ROTATIONAL CONSTANTS

(JT) EV: experimental eigenvalues (dimension 32 in program, but only 14 values present in file)
(JT) BV: rotational constants (dimension 32 in program, but only 14 values present in file)

Annotated input file (“oh.dat”)

Green – found in NIST Chemistry Web Book

        ISTATE
        IENERG |
        IGRAPH | |
        NI NS | | |
TITLE--------------------------------------------- | | | | |
1 OH A DOUBLET SIGMA UPPER STATE 0 1 0 0 2

ZMU-------RMIN------RMAX------DELR------
0.9480871 0.750 3.500 0.005

MAXV
--- BE DE KDMAXV NEIG
  | ----------========== ===---
 12 17.358 35000.00 12

EV(32)
     00.00 1565.99 4554.82 7351.07 9959.53 12392.75 14671.06 16822.54
  18883.03 20896.17 22913.33 24993.67 27204.10 29619.32

BV(32)
   17.3580 16.9606 16.1418 15.2910 14.4082 13.4934 12.5466 11.5678
   10.5570 9.5142 8.4394 7.3326 6.1938 5.0230

FINAL STATE: SAME STRUCTURE AS BEFORE
1 OH X DOUBLET PI GROUND STATE 0 1 0 0 2
0.9480871 0.650 3.500 0.005
 12 18.9108 39162.18 12
      0.00 1847.73 5417.37 8821.40 12061.76 15139.53 18054.80 20806.55
  23392.49 25808.94 28050.69 30110.87 31980.82 33649.91

   18.9108 18.5504 17.8387 17.1366 16.4411 15.7493 15.0581 14.3645
   13.6655 12.9581 12.2394 11.5063 10.7557 9.9849

List of existing input file names

Directory: ATMOS/wrk4/bruno/Mole/Fc

chb.dat chc.dat ch.dat cn.dat mghb.dat mgh.dat nh.dat oh.dat sih.dat
Comparisons

Original from ATMOS/wrk4/bruno/Mole/Fc	F311-generated
1 OH A DOUBLET SIGMA UPPER STATE 0 1 0 0 2 / 0.948087 0.75 3.5 0.005 / 12 17.358 35000 12 / 0 1565.99 4554.82 7351.07 9959.53 12392.8 14671.1 16822.5 / 18883 20896.2 22913.3 24993.7 27204.1 29619.3 / 17.358 16.9606 16.1418 15.291 14.4082 13.4934 12.5466 11.5678 / 10.557 9.5142 8.4394 7.3326 6.1938 5.023 / 1 OH X DOUBLET PI GROUND STATE 0 1 0 0 2 / 0.948087 0.65 3.5 0.005 / 12 18.9108 39162.2 12 / 0 1847.73 5417.37 8821.4 12061.8 15139.5 18054.8 20806.5 / 23392.5 25808.9 28050.7 30110.9 31980.8 33649.9 / 18.9108 18.5504 17.8387 17.1366 16.4411 15.7493 15.0581 14.3645 / 13.6655 12.9581 12.2394 11.5063 10.7557 9.9849	OH A 2 Sigma 0 1 0 0 2 / 0.941883 0.75 3.5 0.005 / 12 17.358 27188.6 12 / 0 1566.2 4559.23 7366.42 9987.78 12423.3 14673 16736.8 / 18614.9 20307.1 21813.4 23133.9 24268.6 25217.5 / 17.358 16.9646 16.1778 15.391 14.6042 13.8174 13.0306 12.2438 / 11.457 10.6702 9.8834 9.0966 8.3098 7.523 / OH X 2 Pi 0 1 0 0 2 / 0.941883 0.75 3.5 0.005 / 12 18.9108 41148.2 12 / 0 1847.66 5415.66 8813.89 12042.4 15101.1 17990 20709.2 / 23258.6 25638.3 27848.2 29888.3 31758.7 33459.3 / 18.9108 18.5487 17.8245 17.1003 16.3761 15.6519 14.9277 14.2035 / 13.4793 12.7551 12.0309 11.3067 10.5825 9.8583
1 MgH A DOUBLET PI UPPER STATE 0 1 0 0 2 / 0.96718516 0.750 5.500 0.005 / 10 6.1913 20541.64 10 / 00.00 791.23 2325.17 3791.25 5185.66 6504.61 7744.30 8900.93 / 9970.70 10949.81 11384.47 12620.89 / 6.1913 6.0949 5.9028 5.7117 5.5216 5.3325 5.1444 4.9573 / 4.7712 4.5861 4.4020 4.2189 / 1 MgH X DOUBLET SIGMA GROUND STATE 0 1 0 0 2 / 0.96718516 0.750 5.500 0.005 / 10 5.8257 17526.60 10 / 0.00 739.67 2171.77 3540.29 4842.07 6071.30 7219.44 8275.23 / 9224.70 10051.18 10735.26 11254.84 / 5.8257 5.7336 5.5515 5.3663 5.1705 4.9566 4.7175 4.4456 / 4.1336 3.7741 3.3598 2.8832	MgH A 2 Pi 0 1 0 0 2 / 0.969696 0.75 3.5 0.005 / 12 6.1913 20541.6 12 / 0 791.314 2327.31 3801.14 5212.8 6562.29 7849.61 9074.76 / 10237.7 11338.6 12377.2 13353.7 14268 15120.1 / 6.1913 6.09475 5.90165 5.70855 5.51545 5.32235 5.12925 4.93615 / 4.74305 4.54995 4.35685 4.16375 3.97065 3.77755 / MgH X 2 Sigma 0 1 0 0 2 / 0.969696 0.75 3.5 0.005 / 12 5.8257 17526.6 12 / 0 739.628 2171.05 3538.69 4842.56 6082.65 7258.96 8371.49 / 9420.24 10405.2 11326.4 12183.8 12977.5 13707.3 / 5.8257 5.73275 5.54685 5.36095 5.17505 4.98915 4.80325 4.61735 / 4.43145 4.24555 4.05965 3.87375 3.68785 3.50195
1 CN B DOUBLET SIGMA UPPER STATE 0 1 0 0 2 / 6.46219329 0.750 3.500 0.005 / 20 1.9730 57951.28 20 / 00.00 1076.90 3200.40 5283.50 7326.20 9328.50 11290.40 13211.90 / 15093.00 16933.70 18734.00 20493.90 22213.40 23892.50 25531.20 27129.50 / 28687.40 30204.90 31682.00 33118.70 34515.00 35870.90 / 1.9730 1.9615 1.9385 1.9155 1.8925 1.8695 1.8465 1.8235 / 1.8005 1.7775 1.7545 1.7315 1.7085 1.6855 1.6625 1.6395 / 1.6165 1.5935 1.5705 1.5475 1.5245 1.5015 / 1 CN X DOUBLET SIGMA GROUND STATE 0 1 0 0 2 / 6.46219329 0.750 3.500 0.005 / 20 1.8997 63620.62 20 / 0.00 1031.02 3073.41 5089.54 7079.36 9042.81 10979.85 12890.41 / 14774.44 16631.89 18462.71 20266.83 22044.20 23794.77 25518.49 27215.29 / 28885.13 30527.95 32143.70 33732.31 35293.75 36827.95 / 1.8997 1.8910 1.8736 1.8561 1.8386 1.8210 1.8033 1.7855 / 1.7677 1.7499 1.7319 1.7139 1.6959 1.6778 1.6596 1.6414 / 1.6231 1.6047 1.5863 1.5678 1.5492 1.5306	CN B 2 Sigma 0 1 0 0 2 / 6.46154 0.75 3.5 0.005 / 20 1.973 57951.3 20 / 0 1076.9 3200.4 5283.5 7326.2 9328.5 11290.4 13211.9 / 15093 16933.7 18734 20493.9 22213.4 23892.5 25531.2 27129.5 / 28687.4 30204.9 31682 33118.7 34515 35870.9 / 1.973 1.9615 1.9385 1.9155 1.8925 1.8695 1.8465 1.8235 / 1.8005 1.7775 1.7545 1.7315 1.7085 1.6855 1.6625 1.6395 / 1.6165 1.5935 1.5705 1.5475 1.5245 1.5015 / CN X 2 Sigma 0 1 0 0 2 / 6.46154 0.75 3.5 0.005 / 20 1.89974 81742.7 20 / 0 1031.02 3073.44 5089.68 7079.75 9043.64 10981.4 12892.9 / 14778.3 16637.5 18470.5 20277.4 22058 23812.5 25540.9 27243 / 28919 30568.8 32192.4 33789.9 35361.2 36906.3 / 1.89974 1.89106 1.87369 1.85632 1.83895 1.82158 1.80421 1.78684 / 1.76947 1.7521 1.73473 1.71737 1.7 1.68263 1.66526 1.64789 / 1.63052 1.61315 1.59578 1.57841 1.56104 1.54368
1 CH A DOUBLET DELTA UPPER STATE 0 1 0 0 2 / 0.92974056 0.750 3.500 0.005 / 10 14.934 25000.00 10 / 00.00 1441.19 4178.59 6722.69 9073.49 11230.99 13195.19 14966.09 / 16543.69 17927.99 19118.99 20116.69 / 14.9340 14.5855 13.8885 13.1915 12.4945 11.7975 11.1005 10.4035 / 9.7065 9.0095 8.3125 7.6155 / 1 CH X DOUBLET PI GROUND STATE 0 1 0 0 2 / 0.92974056 0.750 3.500 0.005 / 10 14.4570 29361.04 10 / 0.00 1413.49 4145.95 6752.37 9232.75 11587.09 13815.39 15917.65 / 17893.87 19744.05 21468.19 23066.29 / 14.4570 14.1900 13.6560 13.1220 12.5880 12.0540 11.5200 10.9860 / 10.4520 9.9180 9.3840 8.8500	CH A 2 Delta 0 1 0 0 2 / 0.923077 0.75 3.5 0.005 / 10 14.934 22216.8 10 / 0 1441.19 4178.59 6722.69 9073.49 11231 13195.2 14966.1 / 16543.7 17928 19119 20116.7 / 14.934 14.5855 13.8885 13.1915 12.4945 11.7975 11.1005 10.4035 / 9.7065 9.0095 8.3125 7.6155 / CH X 2 Pi 0 1 0 0 2 / 0.923077 0.75 3.5 0.005 / 10 14.457 32414.4 10 / 0 1413.49 4145.95 6752.38 9232.75 11587.1 13815.4 15917.7 / 17893.9 19744.1 21468.2 23066.3 / 14.457 14.19 13.656 13.122 12.588 12.054 11.52 10.986 / 10.452 9.918 9.384 8.85